## Slide 1: E-Waste Regulation in West Africa: The Need for A Coherent Approach by Professor ‘Lanre Fagbohun, Ph.D Nigerian Institute of Advanced Legal Studies
At the
Roundtable on E-Waste Regulation in West Africa
24th June, 2015 at the
Nigerian Institute of Advanced Legal Studies
fagbohun@elri-ng.org

## Slide 2: Outline of Discourse
Context of Discourse
Conceptual Life Cycle of EEE
Basis of E-waste Polices, Laws and Regulations
Global Framework of Regulation
Policy Approach Guiding Legal Framework
Regulation of E-waste in West Africa
Indications from Global Best Practices
Conclusion.

## Slide 3: Context of Discourse
Waste Electrical and Electronic Equipment (WEEE) or E-Waste is growing at an exponential rate:
Significant decrease in the cost of technology devices;
Shorter life-span of [mobile phones – 1 to 3 years. Computers – 3 – 4 years; IT accessories – less than 2 years; cameras – 3 to 5 years; TV – 5 to 7 years];
Rapid influx of new products;
Increase in consumer spending power.
WEEE encompass products and appliances that have reached end of life;
WEEE by nature contains toxic materials harmful to humans, non-human species and the environment as well as non-hazardous waste;
The risk of harm is the basis of the need for specialized segregation, collection, transport, treatment and disposal;
West Africa, particularly through Nigeria and Ghana, is a major import hub of e-waste into Africa.

## Slide 4: Conceptual Lifecycle of EEE
EEE
Consumption
Raw Materials Input
Production of EEE
EEE
Sales
WEEE
Generation
WEEE Treatment
WEEE Disposal
Reuse
New Products/ WEEE Residues
Landfill

## Slide 5: Once Trendy… Now Toxic
Microwave
ovens
Electrical irons
Air Conditioners
Mobile Phones
Scanners
Refrigerators
Video Playback and recording systems
Televisions and radio sets
Washing Machines
Keyboards
Electronic games
Computer Monitors
Printers
CPUs
Projectors
PVC wires
Typewriters
Fax Machines

## Slide 6: The Toxic Materials
S/No. | Substances | Effects of Exposure
1. | Arsenic | is a poisonous metallic element which is present in dust and soluble substances. Chronic exposure to arsenic can lead to various diseases of the skin and decrease nerve conduction velocity and can cause lung cancer.
2. | Barium | is a metallic element that is used in sparkplugs, fluorescent lamps and “getters” in vacuum tubes. Being highly unstable in the pure form, it forms poisonous oxides when in contact with air. Short-term exposure to barium could lead to brain swelling, muscle weakness, damage to the heart, liver and spleen.
3. | Beryllium | has been classified as a human carcinogen since exposure to it can cause lung cancer. The primary health concern is inhalation of beryllium dust, fumes or mist. Workers who are constantly exposed to beryllium, even in small amounts, and who become sensitised to it can develop chronic beryllium disease (beryllicosis) - a disease which primarily affects the lungs. Exposure to beryllium causes a form of skin disease that is characterised by poor wound healing and wart-like bumps. Studies have shown that people can still develop beryllium diseases many years after the their last exposure.
4. | Brominated flame retardants (BFRs) | the three main types of BFRS used in electronic and electrical appliances are polybrominated biphenyl, polybrominated diphenyl ether and tetrabromobisphenol - A BFRs have been found in indoor dust and air through migration and evaporation from plastics. Combustion of halogenated case material and printed wiring boards at lower temperatures releases toxic emissions including dioxins which can lead to severe hormonal disorders. Major electronics manufacturers have begun to phase out BFRs because of their toxicity.
Compiled by Lene Ecroignard, e-WASA

## Slide 7: The Toxic Materials…
S/No. | Substances | Effects of Exposure
5. | Cadmium | components may have serious impacts on the kidneys. Cd is adsorbed through respiration and taken up with food. Due to the long half-life in the body, cadmium can easily be accumulated in amounts that cause symptoms of poisoning. Acute exposure to cadmium fumes causes flu-like symptoms of weakness, fever, headache, chills, sweating and muscular pain. The primary health risks of long term exposure are lung cancer and kidney damage.
6. | CFCs (chlorofluorocarbons) | are compounds composed of carbon, fluorine, chlorine, and sometimes hydrogen. Used mainly in cooling units and insulation foam, it has been phased out because when released into the atmosphere, it accumulates in the stratosphere and has a deleterious effect on the ozone layer, which results in an increased incidence of skin cancer in humans and in genetic damage to many other organisms.
7. | Chromium | and its oxides are widely used because of their high conductivity and anti corrosive properties. While some forms of chromium are non toxic, Chromium (VI) is easily absorbed in the human body and can produce various toxic effects within cells. Most chromium (VI) compounds are irritating to eyes, skin and mucous membranes. Chronic exposure to chromium (VI) compounds can cause permanent eye injury, unless properly treated. Chromium VI may also cause DNA damage.
8. | Dioxins and furans | are a family of chemicals comprising 75 different types of dioxin compounds and 135 related compounds known as furans. “Dioxins” refer to the family of compounds comprising polychlorinated dibenzo-p-dioxins and polychlorinated dibenzofurans. Although never intentionally manufactured, dioxins form as unwanted by-products in the manufacture of some pesticides as well as during combustion. They are known to be highly toxic to animals and humans because they bio-accumulate in the body and can lead to malformations of the foetus, decreased reproduction and growth rates and impairment of the immune system, among other things.

## Slide 8: The Toxic Materials…
S/No. | Substances | Effects of Exposure
9. | Lead | is the fifth most widely used metal after iron, aluminium, copper and zinc. It is commonly used in the electrical and electronics industry in solder, lead-acid batteries, electronic components, cable sheathing, in the glass of CRTs, etc. Short-term exposure to high levels of lead can cause vomiting, diarrhoea, convulsions, coma or even death. Other symptoms are appetiteloss, abdominal pain, constipation, fatigue, sleeplessness, irritability and headache. Continued excessive exposure, as in an industrial setting, can affect the kidneys. It is particularly dangerous for young children because it can damage nerves and cause brain and blood disorders.
10. | Mercury | is one of the most toxic yet widely used metals in the production of electrical and electronic applications. It is a toxic heavy metal that bioaccumulates causing brain and liver damage if ingested or inhaled. In electronics and electrical appliances, mercury is concentrated in batteries, some switches and thermostats, mercury vapour and fluorescent lamps.
11. | Polychlorinated biphenyls (PCBs) | are a class of organic compounds use in a variety of applications, including dielectric fluids for capacitors and transformers, heat transfer fluids and as additives in adhesives and plastics.

## Slide 9: The Toxic Materials…
S/No. | Substances | Effects of Exposure
12. | PCBs | have been shown to cause cancer in animals and a number of serious noncancer health effects in animals, including effects on the immune system, reproductive system, nervous system, endocrine system and other health effects. PCBs are persistent contaminants in the environment. Due to the high lipid solubility and slow metabolism rate of these chemicals, PCBs accumulate in the fat-rich tissues of almost all organisms (bioaccumulation). The use of PCBs is prohibited in OECD countries, however, due to its wide use in the past, it still can be found in e-waste and in some other wastes.
13. | Polyvinyl chloride (PVC) | is the most widelyused plastic, used in everyday electronics and appliances, household items, pipes, upholstery etc. PVC is hazardous because it contains up to 56% chlorine which when burned produces large quantities of hydrogen chloride gas, which combine with atmospheric moisture to form hydrochloric acid which when inhaled, leads to respiratory problems.
14. | Selenium | exposure to high concentrations of selenium compounds cause selenosis. The major signs of selenosis are hair loss, nail brittleness, and neurological abnormalities (such as numbness and other odd sensations in the extremities). Source: www.ewaste.ch

## Slide 10: Know Your Stakeholders
Manufacturers/Distributors/Retailers:
New product – Defective products; - Products failing quality tests;
Importers: mix of functional and junk products and appliance;
Individuals households/Business
Generators of WEEE/E-Waste;
Exchange at retailers; pass as gifts; or simply abandons for landfill.
Dissemblers/Dismantlers
Sorting to determine what is for re-sale;
Not-for-resale go for dismantling.
Recyclers
Dismantlers may combine recycling;
There are also large scale smelters for materials recovery.

## Slide 11: Basis of E-Waste Policies , Law and Regulations
Based on the conceptual lifecycles of EEE;
How is WEEE/E-waste defined (broad, narrow)?
What parts of lifecycle is being targeted by the policies, laws and regulations?
Where portion of lifecycle is within geographical boundary, then, the WEEE/E-waste is governed by national policies, laws and regulations;
Where portion of lifecycle falls outside geographical boundary of a country, then, the WEEE/E-waste is governed by international convention.

## Slide 12: Global Framework of Regulation
Basel Convention on the Transboundary Movement of Hazardous Waste and Their Disposal
Adopted March, 1989; entered into force May, 1992;
Objective is to enhance control of the transfrontier movement of toxic waste for environmentally sound management/ reduction;
Core of regulatory system is “prior informed consent” of states of import and transit;
Regional and sub-regional centres for training and technology transfer.
The Basel Ban Amendment of 1995
Premised on complaints against Basel Convention the Basel Ban as of January 1998 banned all forms of hazardous waste exports from OEDC (developed countries) to all non-OECD countries (developing countries);
Block the loophole created by “re-use”;
Not yet entered into force [complete prohibition v. regulated and controlled procedure];
      Source of revenue and raw material
Basel Protocol on Liability and Compensation.

## Slide 13: Global Framework of Regulation…
Stockholm Convention on Persistent Organic Pollutants
Objective is to eliminate or reduce the release of 12 Persistent Organic Pollutants (dirty dozen) from the environment;
Has a mechanism for adding additional chemicals, and for cleaning up existing stockpiles and dumps.
Rotterdam Convention on the Prior Informed Consent Procedure for Certain Hazardous and Pesticides in International Trade
Montreal Protocol on Substances that Deplete the Ozone Layer
To phase out components such as CFCs, halons and methyl chlorofom.

## Slide 14: Global Framework of Regulation…
Convention on the Ban on the Import into Africa and the Control of Transboundary Movement and Management of Hazardous Wastes within Africa (Bamako Convention)
Prohibits the import into Africa of any hazardous waste;
A response to Basel’s encouragement of bilateral, multilateral and regional agreements on hazardous waste;
Seeks to limit trade between African countries and to eliminate it completely between African and non-African countries;
Symbolic treaty without any real legal force [weak government , corruption, differing economic goals]

## Slide 15: Other Initiatives
Durban Declaration on E-Waste Management
Parties to decide their own modus operandi, formulate their actions and choose their response in relation to the E-waste problem. But, recognized: co-operation, creation of awareness, development of policy and legislative framework, promotion of BAT;
Libreville Declaration on Health and Environment in Africa, 2008
Strategic Approach to Integrated Chemical Management’s Expanded Global Action, 2012;
Basel’s Partnership for Action on Computing Equipment (PACE);
UNEP Guidelines on Environmentally Sound Testing, Refurbishment and Repair of Used Computing Equipment;
The Busan Pledge for Action on Children’s Environmental Health;
The Geneva Declaration on E-Waste and Children’s Heath;
Cartegna Declaration on Prevention and Minimization of Hazardous Wastes.

## Slide 16: Policy Approaches Guiding Legal Framework
Extended Producer Responsibility (EPR)
Promotes the “3 Rs”: Reduce, Reuse and Recycle;
Shifts responsibility of safe e-waste recycling pathway from government to producers;
Life Cycle Assessment (LCA)
Cradle-to-grave approach to consider environmental and total impact of a product;
Lack of inventory data is a major problem that undermines the LCA.
Material Flow Analysis (MFA)
Traces a substance from production to application to recycling and disposal;
Very cumbersome to trace substances.
Multi Criteria Analysis (MCA)
Allows for consideration of different solutions and alternatives based on cost and benefits;
For instance, MCA will warn on banning informal recycling.

## Slide 17: Existing Policy Perspectives
European Union has EPR as its fundamental principle;
Japan’s regulations is specific on “Re-use Recycling and Recovery”,
Canada, USA, Australia are moving towards “EPR”;
Africa is also moving towards “EPR”
Limited on influence.

## Slide 18: Elements of Extended Producer Responsibility
Collection Systems -
A national Registry – maintains a register of producers, recyclers, waste organisation and inventory of WEEE;
Logistics – Seeks to address business to consumer (B2C) or business to business (B2B)
    Municipal sites (B2C)
    In-store retailer take back scheme (B2C and B2B)
    Producer take back scheme (B2B).
Collective systems (collects and recycles)
Clearing house system (multiple partners of producers, recyclers and waste management companies provide services on competitive basis.

## Slide 19: Peep into the European Union
Chemical in industrial production are presumed to be innocuous until disproved by scientific study or incident
Chemicals were presumed “innocent until proven guilty
Government to prove guilt on case-by-case basis;
Manifestation of harm years after initial use or exposure.

## Slide 20: Peep into the European Union…
Current approach is captured in RoHs and REACH Directives.
RoHs Directive (Restriction of Hazardous Substances)
EU member states are required to pass national law to ensure that effective 1st July, 2006, new EEE put in the market does not contain lead, mercury, cadmium, hexvalent, chromium, polybrominated biphenyls (PBB) or polybrominated diphenyls ethers (PBDE).
REACH implements risk management through early identification of the intrinsic properties of chemical substances using the tools of: registration, evaluation, authorization and restriction of chemicals.
Current approach is based on Precautionary Principle.

## Slide 21: Peep into the European Union…
The EU Design for reuse (DfRe) framework.
Producers of EEE are required for devices sold in EU jurisdiction not to “prevent through specific design features or manufacturing processes WEEE from being re-used, unless such specific design features or manufacturing process presents overriding advantage in relation to protection of the environment and/or safety requirements”.
    EU Directive 2003/108/EC of 8 December, 2003
While not compelling “design for re-use”, it does “restrains design to prevent re-use”.

## Slide 22: Regulation of E-Waste in West Africa
There are 16 countries that make up West Africa, namely: Benin; Burkina Faso; Ivory Coast; Cape Verde; Gambia; Ghana; Guinea; Guinea Bissau; Liberia; Mali; Mauritania; Niger; Nigeria; Senegal; Sierra Leone; and Togo.
[United Nations scheme of Africa regions includes: the Island of Saint Helena]
[Some listing also include Sao Tome and Principe]
European Commission and UN studies indicate that relative to East and Southern Africa, West Africa is becoming a dumping site for e-waste;
Ghana, Benin, Ivory Coast, Nigeria and Liberia are the hardest hit
  the 2007 Abidjan disaster is still fresh;
  Between 650,000 and one million tons of domestic e-waste are being generated each year;
  Germany and Netherlands are major exporters of end-of-life EEE to West Africa; while UK Netherlands and France dominate seaborne import of data processing equipment.

## Slide 23: Overview of Legislation in Hot spots
Nigeria:
  Ratified Basel Convention, BAN Amendment and Bamako Convention;
  There is the National Environmental (Electrical Electronics Sector) Regulations, 2011 (very broad and extensive on Polluter Pays Principle, EPR etc);
  Harmful Waste (Special Criminal Provisions )Act, 1988;
  Existence of Multi-stakeholder Consultative Committee on E-waste to prepare national policy guidelines/action plan on e-waste management;
  Reactivated The National Toxic Dump Watch Programme (NTCWP);
  Despite all: insufficient enforcement, difficulty in implementing EPR.

## Slide 24: Overview of Legislation in Hot spots …
Ghana:
  Ratified Basel Convention, the BAN Amendment and Bamako Convention;
  Put in place Electronic Waste (Disposal and Recycling) Regulations
  Regulations will require importers of e-waste to pay an e-waste recycling fee on importation???
  Complete ban on importation of electronics more than 5 years old is being considered;
  Designation of disposal assembly points and a code of conduct for the safe disposal of e-waste;
  Despite all: still a major destination for e-waste.

## Slide 25: Overview of Legislation in Hot spots …
Liberia:
  No specific legal instruments relating to e-waste management, thus, reliance is on general policies and legislation on waste management.
Benin:
  No specific legal instrument relating to e-waste management. Approach is similar to that of Liberia.

## Slide 26: Overview of Legislation in Hot spots …
Còte d’Ivoire:
  Party to Basel Convention, Rotterdam Convention, Stockholm Convention;
  There are a number of policy and legal instruments applying directly and indirectly to e-waste management;
  Responsibilities of stakeholders are not defined;
  Opportunities for the development of formal recycling channels are lacking;
  There is the Hazardous Waste Management Plan of the Abidjan District, 2009 with provisions relating to waste market place and guidelines for the take back and valorisation of waste.

## Slide 27: Emerging Facts – Findings of Stakeholder Assessments
Hazardous fractions are still not handled properly during dismantling process, and they are informally dumped or burned;
Extensive employment opportunities arising from collection, recycling and refurbishing are yet to develop into new market niches that combines environmentally safe management;
Low labor costs and lax working conditions continue to create incentive for dumping;
Compromises a strategy of certification of fit for export to or import by developing countries
Many of the countries are still characterised by weak and compromised legal and regulatory systems;

## Slide 28: Emerging Facts – Findings of Stakeholder Assessments…
Lack of a regional approach to monitoring and control of transboundary movement of used and end-of-life equipment and e-waste continue to be a major problem
Substantial import of used EEE are actually non-functional and non-repairable [30% in Ghana, 50% in Benin; 30|% in Nigeria].
Absence of infrastructure for appropriate e-waste management;
Absence of any framework for end-of-life, product take-back or implementation of EPR;
Inadequate public education and awareness.

## Slide 29: Laudable Initiatives
The E-waste Africa Project co-ordinated by the Secretariat of the Basel Convention [Goal is to enhance capacity of West Africa and other African countries to tackle growing problem of e-waste];
The OEMs African Alliance comprising HP, Dell, Nokia, Phillip and UK Recycling Company “Reclaimed Appliance” is facilitating activities with UNEP towards implementing regional solutions [offshoot of E-waste Africa Project].
Enhanced cooperation among government agencies in the area of monitoring e.g. customs, Nigeria Ports Authority, Police and other Security Agencies [Another offshoot of E-Waste Africa Project].
StEP Initiative (solving the E-waste Problem).
  an initiative of various UN organisation working together with industry, government, NGOs and the science sector.

## Slide 30: Best Practices in Regulatory Regimes
Program objectives must be clearly defined;
Collaborative approaches is always helpful in advancing programs;
Market intervention should be transparent, justified and fair and support competition;
Effective stakeholder engagement in program design will ensure smooth implementation;
Effectively designing financial incentives is vital to the success of a scheme. Emphasis on sales-based target do not encourage re-use or design for the environment (limits durability);

## Slide 31: Best Practices in Regulatory Regimes…
A coordinated mechanism which creates incentives and obligations for various players along the supply chain can promote resource efficiency.
Convenience strongly influences consumer behaviour (collection and transport);
Participation of manufacturers in the physical management of their end-of-life products is a significant factor in the success of EPR schemes;
End of life consumer goods should not be viewed as worthless “waste” but as cost effective sources of material.

## Slide 32: Conclusion
A number of tools, mechanisms and measures than can greatly assist in stemming the e-waste problem in West Africa already exist. What is required is for a body like ECOWAS to engender a co-ordinated approach.
A co-ordinated approach will enable the region to amortise the benefits of the different initiatives that abound;
The region should be interested in the development of an international certification scheme that will help differentiate UEEE and WEEE.
Professor Osibanjo has consistently advocated for an ECOWAS e-waste strategy since 2012, and even suggested a draft document for consideration.
Such a document is long overdue.

## Slide 33
THANK YOU